## Slide 1: Basic CSI Photography
Presented by KCSO Photo Unit
Angela Van Liew
(206) 296-3835
angela.vanliew@kingcounty.gov

## Slide 2
Learning objectives:
Understand the basic principles of photography
Understand the value of quality investigation photos
Understand and follow SOP
Know when to ask for help

## Slide 3
Why do we care if we take good photos?
Good photos provide a permanent record of the scene
Good photos tell the story for future investigators and juries

## Slide 4
Four Elements Make Great Photos
  Composition
  Lighting
  Exposure
  Sharpness

## Slide 5
Composition
Choose the best angle, distance, lens
and cropping to tell your story

## Slide 6
Lighting
Lighting is the most important factor in photography
Without light, you have no photos
Types of lighting
Natural (Ambient)
Flash
Flood lights
Flashlights

## Slide 7
Exposure
Choosing the best shutter speed, aperture and ISO to properly record the scene
Auto or Program exposure mode (P) works well for most situations
Large areas of dark or brightness can fool your camera’s meter
The four most common exposure modes are Program (P), Aperture Priority (A), Shutter Priority (S), and Manual (M).

## Slide 8
  Under Exposure
  Over Exposure
  Good Exposure

## Slide 9
Sharpness
Sharpness is a factor of focus, resolution, and depth-of-field
Sharpness is essential for
good crime scene photos
Save the blurry photos
for your art class

## Slide 10
The Camera
The camera is basically a light tight box with a lens for gathering light and a sensor+media to record images.
Most cameras, whether point-and-shoot or dSLR, work quite well using automatic functions (Auto Exposure, Auto Focus, Auto White Balance, Auto Flash)
However, there may be situations where you will need to override those automatic functions

## Slide 11
Basic Camera Parts

## Slide 12
Shutter Speed and Aperture
Work together to:
        Make a good exposure
        Control motion
        Control depth-of-field

## Slide 13
Shutter Speed
Adjusting the length of time the shutter is open is one way
of controlling the amount of light that reaches the camera’s sensor
Shutter speeds of less than 1 second are describe in whole numbers but are actually fractions of a second: 250 = 1/250th of a second
Slow shutter speeds may be necessary in low light situations; use a tripod or some other stabilizer to prevent camera motion and blur
Fast shutter speeds are ideal for stopping motion (camera and subject)

## Slide 14
Fast VS. Slow Shutter Speed

## Slide 15
Aperture
The Aperture, also known as the
lens opening, works much like
the pupil of an eye
Aperture sizes are described as f-stops
The higher the f-stop number,
the smaller the opening
The smaller the f-stop number,
the larger the opening

## Slide 16
Depth of Field
Depth of field (DOF) is the area from near to far
in a scene that is acceptably sharp
DOF is controlled by:
Aperture size
Lens focal length
Distance from subject

## Slide 17
DOF Examples
Shallow DOF (wide open aperture)
Great DOF (small aperture opening)

## Slide 18
Lighting
Along with the photographer and the camera,
lighting is a key element in photography
      Types of Lighting
      Available (Existing)
        Outdoors
        Indoors
      Artificial
        Flash (Strobes)
        Photofloods
        Flashlights
        Quartz-halogen
        Headlights

## Slide 19
      Types of Lighting
  Outdoors at night: headlights
  Outdoors daytime: sunlight

## Slide 20
      Types of Lighting
Flashes or strobes Quartz-halogen
Flashlights

## Slide 21
Lighting Accessories
    Off-shoe flash cord
                Battery packs
                Light modifiers

## Slide 22
Break Time?