## Slide 1
BASIC LAW ENFORCEMENT ACADEMY
WASHINGTON STATE
CRIMINAL JUSTICE TRAINING
HAZARDOUS MATERIALS

## Slide 2
FIRST RESPONSE

## Slide 3: You get hundreds of chances to do it right, only one to do it wrong !

## Slide 4: In the the old days. . . . .

## Slide 5: What Do I Do Now ?

## Slide 6: Common Sense ?
Upwind
Uphill
Upstream

## Slide 7: More common sense
Isolate
Deny Entry
Evacuate
Shelter in Place

## Slide 8: Isolate and Deny Entry:
Establish control of the scene by keeping everyone away from the area if they are not directly involved in the emergency response operation.

## Slide 9: Evacuate:
Move all people from a threatened area to a safer place. To perform the evacuation you must have enough time for:
1. Warn people of the evacuation.
2. Allow the people to get ready to evacuate.
3. Leave the area

## Slide 10: Shelter in Place:
Retaining people inside a building until the danger of a short-term spill or toxic vapor cloud passes. Personnel are moved to the center of the building and the HVAC system is turned off. Shelter in place is used when evacuating the public would cause greater risk than staying where they are, or when an evacuation cannot be performed.

## Slide 11
1. Protect your health and safety during a HAZMAT incident.
2. Recognize hazardous materials.
3. Prevent or minimize exposure to hazardous materials.
4. Come home alive and live to collect a well earned retirement.
The Key Learning Goals for The First Responder

## Slide 12: Emergency Response Regulations
Environmental - U.S. Environmental Protection Agency
Washington Department of Ecology
USEPA: 33 CFR and 40 CFR
Health & Safety - U.S. Department of Labor (OSHA)
Washington Department of Labor & Industries
(DISH-WISHA) DISH: WAC 296 - 62 OSHA: 29 CFR
Transportation - U.S. Department of Transportation
USDOT: 49 CFR
Fire Protection - National Fire Protection Agency
NFPA 471, 472, 474

## Slide 13
1. Define learning goals for the course.
2. Identify four major categories of sites where HAZMAT emergencies occur.
3. Name at least five different substances classified as hazardous materials.
4. Explain how an incident’s location indicates the type and quantity of hazards present.
5. Identify hazards involved with sites such as schools, hospitals, and manufacturing plants.
6. Apply the APIE process to management of hazardous materials incidents.
Key Learning Goals :
Common Alarms Summary

## Slide 14
… because common alarms are HAZMAT incidents. You can be exposed to hazardous materials any time you respond to any incident.
    1. Why is this section called Common Alarms?
2. Name the four main categories where HAZMAT emergencies may occur.
Commercial Fixed Sites
Non-Structural Locations
Transportation Corridors
Residences
2

## Slide 15
?
    Name at least five substances classified as hazardous materials.
Gasoline
Propane
Chlorine
Acids
Benzene
Pesticides
Fertilizers
Paint
Explosives
1

## Slide 16
2. What are the health and safety challenges at this type of site?
1. What hazardous materials might be involved at these sites?
    Here is an incident at a Commercial Fixed Site.
0

## Slide 17
What hazardous materials might be involved at this type of site?
What are the health and safety challenges at this type of site?
    Here is an incident at a Non-Structural Location.
0

## Slide 18
What hazardous materials might be involved at these sites?
What are the health and safety challenges at these sites?
    Here is an incident at a Residence.
0

## Slide 19
What hazardous materials might be involved at these sites?
What are the health and safety challenges at these sites?
    Here is an incident in a Transportation Corridor.
0

## Slide 20
First Responder Actions (FRAs) define this process.
This process repeats itself until the mission is accomplished.
STEP 1. Analyze the Problem
FRAs:
• Establish command
• Survey the scene
STEP 2. Plan the Response
FRAs:
• Collect and interpret information
• Assess vulnerable population
• Identify container damage
STEP 3. Implement the Plan
FRAs:
• Create and implement a specific plan
• Isolate the hazard
STEP 4. Evaluate the Progress
FRAs:
• Continue to evaluate
    The APIE Process is a four-step process.
4

## Slide 21
http://www.youtube.com/watch?v=VO3rwU74xN0

## Slide 22
http://www.youtube.com/watch?v=pw_bnS-qcds

## Slide 23
1. Identify four basic clues for the presence of hazardous materials.
2. Use occupancy and location clues to identify hazardous materials.
4. Identify HAZMAT marking systems.
5. Use 2012 ERG and shipping papers to identify hazardous materials.
6. Identify basic physical properties of hazardous materials.
Key Learning Goals :
Recognition & Identification
3. Identify highway cargo tanks and
rail tank cars.

## Slide 24: General precautions
Don’t “rush in” Think First
Be Selfish
Approach from up-wind, up-hill. Up stream
Stay clear of all spills, vapors, fumes & smoke.

## Slide 25: More Safety Precautions
Approach cautiously from up-wind.
Secure the scene, deny entry.
Identify hazards.
Perform a “Risk Assessment”.
Obtain assistance.
Decide upon site entry.
Respond. IN AN APPROPRIATE MANNER.

## Slide 26: More Safety Precautions
DO NOT !
  WALK INTO or TOUCH SPILLED MATERIALS.
  AVOID INHALATION OF FUMES, SMOKE AND VAPORS.
  ODORLESS GASES OR VAPORS MAY BE HARMFUL.

## Slide 27: Who you gonna call…hazbusters
Your local response organization.
State, County emergency groups.
Shipper, transporter, or receiving party.
National assistance: CHEMTREC, CANUTEC.

## Slide 28: What Information do you need to have?
Your name, call back telephone or FAX number.
Location & nature of the problem.
Name & UN identification number.
Shipper, consignee/point of origin.
Carrier name, rail car or truck number.
Container type & size.
Quantity of material transported or released.
Local conditions.
Injuries & exposures.
Local ERP that have been notified.

## Slide 29: Information Sources

## Slide 30: Important Phone Numbers
911
CHEMTREC : 1-800-424-9300
CANUTEC : 613-996-6666
DEFENSE DEPT. : 703-697--0218
INFOTRAC : 1-800-535-5053
CHEM-TEL : 1-800-255-3924
3E COMPANY : 1-800-451-8346

## Slide 31: Emergency Response Guide
Department of Transportation
Updated every Four (4) Years

## Slide 32: The ERG is updated every four years to accommodate new products and technology. The 2012 ERG will have new, revised and expanded sections, including:
An updated dangerous goods list that includes all hazardous materials added to the UN Recommendations on the Transport of Dangerous Goods since the last edition of the book
An index of dangerous goods in order of ID number
An index of dangerous goods in alphabetical order
A rail car identification chart
A road trailer identification chart
Information on pipeline safety

## Slide 33: How to Use the Guidebook

## Slide 34: Guidebook Contents
Yellow-bordered pages : index list of dangerous goods in numerical order of ID number.
Blue-bordered pages : index of dangerous goods in alphabetical order of material name.
Orange-bordered pages : emergency response guides.
Green bordered pages : isolation & evacuation tables.

## Slide 35: Pipeline Safety Information

## Slide 36: The “Yellow Pages”
List of chemicals by UN Identification number.
Highlighted entries indicate materials that are found in the green pages.
If these materials are on fire, or a fire is involved, go to the orange guide book pages.

## Slide 37: The “Yellow Pages”

## Slide 38: The “Blue Pages”
List of chemicals by alphabetical order.
Highlighted entries indicate materials that are found in the green pages.
If these materials are on fire, or a fire is involved, go to the orange guide book pages.

## Slide 39: The “Blue Pages”

## Slide 40: Exercise
What guide is used for a spill of caustic soda ?
What is the UN # ?
What type of extinguishing agent can be used on a large metal-hydride fire ?

## Slide 41: The “Orange Pages”
The emergency action guide pages, the meat and potatoes of this resource guide.

## Slide 42: The “Orange Pages”

## Slide 43: Green-bordered Pages
Lists by ID # “toxic inhalation hazard” ( TIH ) materials.
Initial and protective action distances.
Distances listed for small & large spills.
Sub-divided into daytime & night time events.

## Slide 44: Green-bordered Pages

## Slide 45: Initial Isolation Distance
That distance within which all persons should be considered
for evacuation in all directions from the actual spill or leak source.
860 meters
Compressed gas,
toxic, n.o.s., ID 1955,
Inhalation zone A.
Small spill = 430 meters,
therefore representing an
evacuation circle of 860 m.

## Slide 46: Protective Action Distance
That distance within which all persons should be considered
for evacuation downwind from the actual spill or leak source.
Compressed gas,
toxic, n.o.s., ID 1955,
Inhalation zone A.
daytime spill = 4.2 kilometers,
nighttime spill representing
an evacuation zone of 8.4 km..
4.2 Km

## Slide 47: The Rule of “Double Double”
Whenever the Incident Commander, in the interest of public safety deems it necessary to expand the listed isolation distances, he or she should do so.
The rule of Double Double may apply.

## Slide 48: The “Green Pages”
Isolation and protective action guide.
Likely effected area 30 minutes after spill occurs.
Initial isolation zone - surrounding area.
Protective action zone - downwind area.
When in doubt - “Double Double”.

## Slide 49: The “Green Pages”
The dangerous goods.
  Degree of health hazard, amount involved, containment/control of release, rate of vapor movement.
The population threatened.
  Location, time available to evacuate or shelter in-place, ability to control evacuation or shelter in-place, building types/availability, special populations.
Weather conditions.
  Effect on vapor/cloud movement, potential for change, effect on evacuation or shelter in place.

## Slide 50: Exercise
You arrive on location and observe an orange placard on the rear of a smoking cargo container. What is the material classification ?
What guide pages do you reference ?

## Slide 51: Self Preservation

## Slide 52: The “Back of the Book”
Definitions of Personal Protective Clothing.
Fire and Spill Control.
Chemical and Biological agent events.
  Differences between them.
  Indicators of their presence in an event.
Personal Safety Considerations.
Glossary

## Slide 53: EMERGENCY RESPONSE TELEPHONE NUMBERS
UNITED STATES
1. CHEMTREC® 1-800-424-9300 (Toll-free in the U.S, Canada, and the U.S. Virgin Islands) 703-527-3887 For calls originating elsewhere (Collect calls are accepted)
2. CHEM-TEL, INC. 1-800-255-3924 (Toll-free in the U.S, Canada, and the U.S. Virgin Islands) 813-248-0585 For calls originating elsewhere (Collect calls are accepted)
3. INFOTRAC 1-800-535-5053 (Toll-free in the U.S, Canada, and the U.S. Virgin Islands) 352-323-3500 For calls originating elsewhere Collect calls are accepted)
4. 3E COMPANY 1-800-451-8346 (Toll-free in the U.S, Canada, and the U.S. Virgin Islands) 760-602-8703 For calls originating elsewhere (Collect calls are accepted)
5. MILITARY SHIPMENTS 703-697-0218 - Explosives/ammunition incidents (Collect calls are accepted) 1-800-851-8061 - All other dangerous goods incidents

## Slide 54: CONTAINER SHAPES & SIZES
Type 1.
Bulk Containers
Type 2.
Non-Bulk Containers
Type 3.
Intermediate Bulk Containers (IBCs)
The Department of Transportation (DOT) classifies three types of containers:
  Type 1: Bulk Containers
  Bulk container capacities, except for watercraft are:
  A maximum capacity of more than 119 gallons of liquids
  A maximum net capacity of more than 882 pound of solids
  A water capacity greater than 1,001 pounds for gases

## Slide 55
Tube trailers carry from 2 to 20 long cylinders that are permanently mounted on a semi-trailer.
Transport compressed gases such as:
  Argon
  Helium
  Carbon dioxide
  Hydrogen
  Oxygen
Tube Trailers
Permanently Mounted Cylinders
0

## Slide 56: Pressure Cargo Tanks
Circular cross-section and round ends
Top 2/3 of the tank is highly reflective or painted white
Tanks transport liquefied gases, such as:
  Anhydrous ammonia
  Butane
  Propane
  Chlorine
Circular, Rounded End
Reflective or Painted White
0

## Slide 57: Corrosive Liquid Cargo Tanks
Circular cross-sections and flat ends
Relatively small diameter
Tanks usually have visible ring stiffeners, although an outer metal “skin” may be present
Tanks transport high-density liquids, such as:
  Sodium hydroxide
  Sulfuric acid
  Hydrochloric acid
Circular, Flat End
Stiffening Rings
0

## Slide 58: Low Pressure Cargo Tanks
Horseshoe shaped cross-sections with circular, flat ends May have rollover protection
Tanks transport:
  Flammable or
  combustible liquids
  Mild corrosives
  Poisons
  Many other liquids
Circular, Flat End
Stiffening Rings
0
Rollover Protection

## Slide 59: Non-Pressure Cargo Tanks
Elliptical cross-section with flat ends
Usually has more than one compartment
Tanks transport petroleum products such as:
  Gasoline
  Fuel oil
  Jet fuels
Elliptical Cross-Section, Flat End
Compartment 3
Compartment 1
Compartment 2
0

## Slide 60: Dry Bulk Commodity Carriers
Carriers have large sloping, v-shaped unloading compartments. Transport dry chemicals such as:
Fertilizers
Oxidizers
V-Shaped Unloading Compartments
0

## Slide 61: ROAD TRAILER IDENTIFICATION CHART

## Slide 62
Type 1.
Bulk Containers
Type 2.
Non-Bulk containers
Type 3.
Bulk Portable Containers and Intermediate Bulk Containers
CONTAINER SHAPES & SIZES
Type 1: Bulk Containers -
Railroad Tank Cars
Railroad tank cars transport hazardous and non-hazardous materials.
Most carry only a single commodity.
Railroad personnel are the best source of information during rail incidents.
The Department of Transportation (DOT) classifies three types of containers:

## Slide 63
Corrosive Liquid Tank Car
Similar to non-pressure tank cars
Can be distinguished by staining around manway
Some painted with vertical stripe of corrosion-resistant paint
Vertical Stripe of Corrosion-Resistant Paint
0

## Slide 64: Non-Pressure Railroad Tank Cars
Non-Pressure Tank Cars (or general service cars) have visible valves and fittings at top of tank
Transport:
  Flammable liquids
  Flammable solids
  Oxidizers
  Organic peroxides
  Poisons
  Non-hazardous materials
  Corrosive liquids
Valves and fittings at top of tank
Manway
0

## Slide 65: Pressure Tank Cars
Consists of protective housing at the top center Transports flammable, non-flammable, and poisonous compressed gases such as:
  Chlorine
  Propane
  Anhydrous ammonia
Protective Housing at Top Center
0

## Slide 66: Other Railroad Cars
Other types of rail cars that transport hazardous materials include:
  Trailer on flat cars (TOFC)
  Container on flat cars (COFC)
  Box cars
  Gondola cars
  Hopper cars
  Tube trailer cars
0

## Slide 67
Cryogenic Liquid Tank Car
Carries low-pressure refrigerated liquids (minus 130˚F and below)
Designed as a tank-within-a-tank for insulation
Product may vent under normal conditions
Tank-Within-a-Tank
0

## Slide 68: RAIL CAR IDENTIFICATION CHART

## Slide 69
CONTAINER SHAPES & SIZES
Type 1.
Bulk Containers
Type 2.
Non-Bulk Containers
Type 3.
Bulk Portable Containers and Intermediate Bulk Containers
Type 3: Bulk Portable Containers & Intermediate Bulk Containers
Types of bulk containers include:
  Ton Containers
  Intermodals
  Intermediate Bulk Containers (IBCs) or Totes
The Department of Transportation (DOT) classifies three types of containers:

## Slide 70: Bulk Portable Containers and Intermediate Bulk Containers
TON CONTAINERS transport:
Anhydrous ammonia, Butadiene, Chlorine, Phosgene, Sulfur dioxide, Refrigerant gases
INTERMODAL TANK CONTAINERS (IMs): single metal tank mounted inside a sturdy metal supporting frame.
Transport LP gases, Flammable gases, Anhydrous ammonia
INTERMEDIATE BULK CONTAINERS (IBCs) or TOTES: aluminum, stainless steel, or poly materials
Transport most hazardous materials classifications
Rigid or flexible portable packaging designed for mechanical handling
0

## Slide 71: ID CODES for INTERMODAL CONTAINERS
33
1203

## Slide 72: INTERMODAL CONTAINERS

## Slide 73: ID CODES for INTERMODAL CONTAINERS
2 - Emission of gas due to pressure or chemical reaction.
3 - Flammability of liquid vapor/gases or self heating.
4 - Flammability of solids or self heating liquid.
5 - Oxidizing effect.
6 - Toxicity or risk of infection.
7 - Radioactivity
8 - Corrosivity
9 –Miscellaneous Dangerous Substance

## Slide 74: ID CODES for INTERMODAL CONTAINERS
Por ejemplo…
  X839 => X 8 3 9
  X = material will react dangerously w/ water.
  8 = corrosive
  3 = flammable liquid, gas or self heating liquid
  9 = risk of spontaneous violent reaction

## Slide 75: Exercise
Go to guide 111 (Page 168).
What types of materials are referenced to this page ?

## Slide 76
CONTAINER SHAPES & SIZES
Type 2: Non-Bulk Containers include:
1. Drums
2. Pails
3. Bags or sacks
4. Fiberboard boxes
5. Carboys
6. Cylinders
7. Dewars
8. Multi-cell packages
Type 1.
Bulk Containers
Type 2.
Non-Bulk Containers
Type 3.
Bulk Portable Containers and Intermediate Bulk Containers
The Department of Transportation (DOT) classifies three types of containers:

## Slide 77
Non-Bulk Containers
1. DRUMS: steel, fiberboard, or poly materials
Transport several HAZMAT classifications.
2. PAILS: steel, fiberboard, or poly materials
Hold one to five gallons of flammable liquids, poisons or oxidizers.
3. BAGS or SACKS: paper or plastic
Holds dry corrosives, blasting agents, explosives, flammable solids, oxidizers, organic peroxides, poisons, or ORMs.
4. WOODEN BOXES transport every hazardous materials class, except compressed gases.
FIBERBOARD BOXES are used for everything, except compressed gases and poisons.
0

## Slide 78
8. MULTI-CELL PACKAGES
Usually polystyrene form-fitted containers with no more than six bottles holding four liters.
5. CARBOYS: plastic, metal or glass.
Transport corrosives.
6. CYLINDERS contain compressed gases, flammable/ combustible liquids, poisons, radioactive materials, and corrosives.
7. DEWARS used for the storage of cryogenic materials, such as: Liquid nitrogen, Oxygen, Helium, and Argon.
Non-Bulk Containers
0

## Slide 79
TYPE 1: Bulk Containers - Fixed-site Bulk Containers have certain characteristics that identify them as non-pressurized, low pressure, or pressurized. Pressurized tanks have rounded ends and visible pressure relief valves. Non- and low pressurized tanks generally have flat ends; pressure relief devices will not be present.
CONTAINER SHAPES & SIZES
Type 1.
Bulk Containers
Type 2.
Non-Bulk Containers
Type 3.
Bulk Portable Containers and Intermediate Bulk Containers
The Department of Transportation (DOT) classifies 3 types of containers:

## Slide 80
Fixed Site Bulk Containers
Vertical Flat Roof Tank
Circular with a flat roof
Cone Roof Tank
Circular with a cone-shaped roof
Open Floating Roof Tank
Roof floats on contents; may have ladder on sIde
Dome Roof Tanks
Vertical structure with dome-shaped roof with internal pressure up to 15 psi
Covered Floating Roof Tank
Cone-shaped roof covers inner floating roof with large vents at top
0

## Slide 81
Horizontal Tank
Restricted or banned due to possible tank/leg failure
Underground Storage Tank
Gauges and controls are above ground
Pressurized Horizontal Tank
Usually set on legs or blocks; painted white or reflective color; pressure relief devices on top
Spherical Tank
Ball-shaped; painted white or reflective color
Cryogenic Liquid Storage Tank
Vertical structure with dome-shaped roof; internal pressure up to 15 psi
Fixed Site Bulk Containers
0

## Slide 82
TYPES 1, 2, and 3: RADIOACTIVE MATERIAL CONTAINERS are made of any number of materials. Low-level radioactive materials are often packaged in glass bottles, then packaged in cardboard, fiberboard, wooden boxes or steel drums. High-level radioactive materials are packaged in steel containers lined with lead, paraffin, and/or depleted uranium.
CONTAINER SHAPES & SIZES
Type 1.
Bulk Containers
Type 2.
Non-Bulk Containers
Type 3.
Bulk Portable Containers and Intermediate Bulk Containers
The Department of Transportation (DOT) classifies 3 types of containers:

## Slide 83
TYPE B PACKAGING
Used to transport materials that would be a hazard if released
TYPE A PACKAGING
Tested for ability to contain contents; made of fiberboard, wood, or steel
INDUSTRIAL PACKAGING
Low levels of radioactivity; safer for normal transportation activities
EXCEPTED PACKAGING
Low levels of radioactivity; shipped in limited quantities
Radioactive Materials Containers
0

## Slide 84
Marking Systems
Marking Systems provide information about types and hazards of products being stored or transported.
The most common marking systems are:
  DOT system for
  materials in transit
  NFPA 704 system
  for fixed sites
3
4
OX
3

## Slide 85
DOT Labels are:
Diamond shaped; 4” on each side
On two sides of the container near the shipping name of the material
Secondary hazards must be labeled
DOT Placards are:
Diamond-shaped; 10 3/4” on each side
Affixed to both sides and ends of the vehicle
DOT placards & labels generally indicate a primary hazard.
DOT Placards & Labels
10 3/4” diamond- shaped placard
4” diamond-shaped labels
0
PROBLEMS with DOT Marking:
Secondary hazards may not be identified
Degree or severity of a hazard is not apparent for most classes
Enforcement is difficult

## Slide 86
DOT Marking System
PLACARDS are required for Secondary Hazards that are:
Poisonous by inhalation
Dangerous when wet
Other specific chemicals
0
        UNITED NATIONS (UN) ID NUMBERS:
        Four-digit ID numbers can replace text on placards for bulk shipments of hazardous materials. However, it cannot replace the DANGEROUS placard or the class name for Radioactive or Explosive materials.
UN identification numbers can be posted on a separate orange panel next to a placard.
UN identification numbers can be incorporated into a DOT placard.
3257
2448
4” black numbers on orange panel next to a placard
In the center of the placard
Or, in the center of placard-sized white diamond when no other placard is required
1075

## Slide 87
There are nine classes in the DOT marking system.
Some classes are broken down into divisions.
Class 1: Explosive
Class 3: Flammable/ Combustible Liquid
Class 9: Miscellaneous Dangerous Material
Class 6: Poison
Class 5: Oxidizer/ Organic Peroxide
Class 4: Spontaneously Combustible
Class 7: Radioactive
Class 2: Gases
Class 8: Corrosive Material
DOT Marking System
0

## Slide 88
Table 1 Materials
Table 1 materials must always be placarded with their primary hazard placards, regardless of the amount being transported.
The categories are:
Explosive 1.1
Explosive 1.2
Explosive 1.3
Poisonous Gas (Class 2.3)
Dangerous When Wet (Class 4.3)
Organic Peroxides, Type B, Temperature Controlled (Class 5.2)
Poison Inhalation Hazard, Zone A or B (Class 6.1)
Radioactive (Class 7; those substances in Radioactive III packaging only)

## Slide 89
EXAMPLES: TNT, Dynamite, Black powder
DOT Marking System
CLASS 1: Explosives — 6 divisions
Orange = explosive
Bursting ball = explosive
0

## Slide 90
CLASS 2: Gases — 4 divisions
EXAMPLES: Argon, Chlorine, Helium, Nitrogen, Oxygen, Propane
DIVISION 2.2:
Green = non-flammable gas
Cylinder = non-flammable gas
DIVISION 2.1:
Red = flammable/ combustible
Flame = flammable
DIVISION 2.3:
Skull & crossbones = poison
White = poisonous material
DOT Marking System
0
OXYGEN: may be used in lieu of non-flammable placard
Flaming circle = oxidizer
Yellow = oxygen

## Slide 91
CLASS 3: Flammable or Combustible Liquids — 4 divisions
EXAMPLES: Gasoline, Diesel fuel, Acetone
DOT Marking System
0
FLAMMABLE
For all CLASS 3:
Red = flammable/ combustible
Flame = flammable

## Slide 92
EXAMPLES: Nitrocellulose, Magnesium turning, Calcium carbide, Potassium, Sodium metal, Self-heating material
CLASS 4: Flammable Solids, Spontaneously Combustible & Dangerous When Wet
DIVISION 4.2:
White over red = spontaneous combustion
Flame = flammable
DOT Marking System
DIVISION 4.1:
White with red stripes = flammable solid
Flame = flammable
DIVISION 4.3:
Blue = dangerous when wet
Flame = flammable
0

## Slide 93
OXIDIZER (5.1) EXAMPLES: Hydrogen peroxide, Potassium nitrate, Sodium persulfate
DIVISIONS 5.1 & 5.2:
Yellow indicates oxidizer (including oxygen) or organic peroxide
Circle with flame indicates oxidizing material or organic peroxide
CLASS 5: Oxidizer/Organic Peroxide
DOT Marking System
0
ORGANIC PEROXIDE (5.2) EXAMPLES: Dibenzoyl peroxide, Methyl ethyl ketone peroxide (MEKP), Peroxyacetic acid

## Slide 94
EXAMPLES: Chloropicrin (tear gas), Arsenic
CLASS 6: Poison
DOT Marking System
KEEP AWAY FROM FOOD:
White = poisonous material
St. Andrew’s Cross over wheat shaft = keep away from foodstuffs
6
DIVISION 6.1:
White = poisonous material
Skull & crossbones = poisonous material
POISON:
White = poisonous material
0

## Slide 95
CLASS 7: Radioactive
DOT Marking System
EXAMPLES: Cobalt, Uranium hexafluoride, Yellow cake,
Nuclear pharmaceuticals (Gallium and Thallium)
*
CLASS 7:
Yellow over white = radioactive material
Trefoil (propeller) = radioactive material
0

## Slide 96
CLASS 8: Corrosive Materials
DOT Marking System
EXAMPLES: Sulfuric acid, Nitric acid, Hydrochloric acid, Sodium Hydroxide
CLASS 8:
White over black = corrosive
Test tube and hand/metal symbol = corrosive
0

## Slide 97
CLASS 9: Miscellaneous Dangerous Material
DOT Marking System
EXAMPLES: Dry ice, Molten sulfur, PCBs (electrical transformers)
CLASS 9:
Black stripes over white indicates miscellaneous hazardous material
0

## Slide 98
DANGEROUS Placard
DOT Marking System
Red with white band = dangerous
EXAMPLES: Used if two or more Table 2 materials with a combined weight of more than 1,001 lbs. are being transported.
0

## Slide 99
Based upon this NFPA diamond, what can you predict for potential hazards?
The NFPA Marking System uses a diamond divided into four color-coded areas with numerals that indicate a degree of hazard.
NFPA Marking System
Lowest Hazard 0 1 2 3 4 Greatest Hazard
3
3
4
OX
NFPA Marking System Key (Scale 0 to 4)
1
RED = Flammability Hazard
BLUE = Health Hazard
WHITE =
Special Hazard
YELLOW = Reactivity Hazard

## Slide 100
Other Marking Systems
EPA requires pesticides labeling by health risk:
  Danger = Highest
  Warning = Medium
  Caution = Lowest
A company name may indicate the hazards that are present.
Trailer numbers, telephone numbers, license plate numbers are useful in identifying materials.
The name of specific hazardous materials are sometimes stenciled on the side of tank cars.
Companies may adopt their own marking systems for containers.
Can you think of other types of marking systems in your community that are used in identifying hazardous materials?
6

## Slide 101: The Future The HAZCOM Standard is now aligned with the Globally Harmonized System of Classification and Labeling of Chemicals (GHS).

## Slide 102: Pictograms Vs. DOT Labeling
Should not be confused with one anotherDot Labels convey Hazard Info during transportation
GHS Pictograms convey Hazard Info while in use

## Slide 104
1. Identify four basic clues for the presence of hazardous materials.
2. Use occupancy and location clues to identify hazardous materials.
4. Identify HAZMAT marking systems.
5. Use 2012 ERG & NIOSH Pocket Guides, facility documents and shipping papers to identify hazardous materials.
6. Identify basic physical properties of hazardous materials.
Key Learning Goals :
Recognition & Identification Summary
3. Identify highway cargo tanks and
rail tank cars.

## Slide 105
1. Occupancy and Location
2. Container Shapes and Sizes
4. Shipping Papers and Facility Documents
3. Marking Systems
What are the four basic clues used to recognize the presence of hazardous materials?
1

## Slide 106: Recognition and Identification Clues
Identify at least two types of occupancies that might indicate the presence of hazardous materials.
1
Industrial Locations
Residential

## Slide 107: Recognition and Identification Clues
Non-Bulk Household Products
Identify at least two types of containers that might indicate the presence of hazardous materials.
3
Low Pressure Tanker
Type A Radioactive Packaging

## Slide 108: Recognition and Identification Clues
Material Safety Data Sheets
Identify at least two types of shipping papers and facility documents used to recognize the presence of hazardous materials.
Bill of Lading or Freight Bill
Waybill and/or Consist
Dangerous Cargo Manifest
Air Bill
1

## Slide 109: Recognition and Identification Clues
DOT system for materials in transit
The NFPA 704 system for fixed sites
Which marking system is used for materials in transit and which for fixed sites?
1

## Slide 110
1. What are three types of products this non-pressure highway carrier might be carrying?
  Gasoline
  Fuel oil
  Jet fuels
2. What types of products might this non-pressure railroad tank car be carrying?
Flammable liquids
Oxidizers
Organic peroxides
Poisons
Corrosive liquids
Non-hazardous materials
Shipping Containers
2

## Slide 111
2. Although this gondola car transports bulk ores and other solid materials,
….what carcinogenic material does it often carry?
1. What types of hazardous materials may be shipped in TOFCs or COFCs?
Container on Flat Car (COFC)
Trailer on Flat Car (TOFC)
Gondola Car
    Radioactive materials
There are no Federal Railroad Administration (FRA) restrictions specifying what hazard classes may be shipped in TOFCs or COFCs .
Shipping Containers
2

## Slide 112
Which document contains in-depth information on physical properties,
toxicity, and personal protective equipment
Which document is designed for use in transportation incidents and provides information on common hazardous materials
ERG & NIOSH Guidebooks
1

## Slide 113
1. STATES OF MATTER:
Substances can change from one state to another as changes occur in temperature or pressure, or both.
Why would a toxic substance be more hazardous in the gaseous state than in the liquid state?
Because it is easier to inhale as a gas and more difficult to control.
2. FLASH POINTS:
Which has a higher flash point - a flammable liquid or a combustible liquid?
A combustible liquid has the higher flash point - above 141˚F, below 200˚F. Flammable liquid’s flash point is less than 141˚F.
3. VAPOR DENSITY:
Air has a vapor density of 1. When released into the air, what happens to a substance with a vapor density greater than 1?
It will sink, staying close to the ground.
It will sink, staying close to the ground.
It will sink, staying close to the ground.
It will sink, staying close to the ground.
It will sink, staying close to the ground.
ERG & NIOSH Guidebooks
3

## Slide 114
1. Describe how and why a release of chlorine gas from a one-ton cylinder at a community’s water treatment facility might affect the surrounding area.
2. When oxidizers are added to other materials, they dramatically accelerate combustion. Oxidizers often continue to burn even after sources of air are removed. Why?
ox•i•dize (verb): combine with oxygen
Because oxidizers provide their own oxidizing capability and need no air to burn.
3. Cryogenic gases are compressed and have very low temperatures.
During a fire, why would you not spray a cryogenic container with water?
Water may freeze the structure and crack the container.
Evacuate the area; wind direction is a factor; vapor density is heavier than air; check topography; a little liquid chlorine turns into a much greater volume of gas.
ERG & NIOSH Guidebooks
3

## Slide 115
THE END
Use the four basic recognition and identification clues to detect the presence of hazardous materials.
Lessons Learned
Understand the importance of the physical properties of hazardous materials to predict chemical reactions at the scene of an incident.
Use available resources to identify specific hazards of materials
involved in an incident.
3

## Slide 116: Summary
Identify the material.
Look up the material’s 3-digit guide number.
Turn to the numbered guide.
If there is there is nothing else, use the placard pages.
If a reference cannot be found, use guide 111.

## Slide 117: Summary
Yellow-bordered pages : index list of dangerous goods in numerical order of ID number.
Blue-bordered pages : index of dangerous goods in alphabetical order of material name.
Orange-bordered pages : emergency response guides.
Green bordered pages : isolation & evacuation tables.

## Slide 118: Summary
Approach cautiously from up-wind.
Secure the scene, deny entry.
Identify hazards.
Perform a “Risk Assessment”.
Obtain assistance.
Decide upon site entry.
Respond. IN AN APPROPRIATE MANNER.

## Slide 119: Summary
DO NOT !
  WALK INTO or TOUCH SPILLED MATERIALS.
  AVOID INHALATION OF FUMES, SMOKE AND VAPORS.
  ODORLESS GASES OR VAPORS MAY BE HARMFUL.

## Slide 120
1. Explain exposure and contamination.
2. Identify the purpose of medical surveillance.
3. Explain decontamination procedures.
4. Explain limitations and proper care of Personal Protective Equipment (PPE).
5. Describe four major routes of entry of hazardous materials.
6. List ways to prevent/minimize exposure to hazardous materials.
Health & Safety Summary
Key Learning Goals :

## Slide 121
Your health assessments are based on:
  Diagnostic medical testing
  Biological monitoring
  Questionnaire data
  Physical exams
... to detect early changes in health status so permanent health effects can be prevented.
What is the purpose of medical surveillance ...?
1
CFR 1910.120 cites these conditions when fire fighters must be provided with a medical surveillance program:
When they operate as members of a HAZMAT Team.
When exposed to hazardous substances for 30 or more days per year at, or above, exposure limits set by OSHA.
When injured due to overexposure from an emergency incident involving hazardous substances.
Your physician needs the following information:
  A copy of 29 CFR 1910.120
  Your job duties
  Previous exposures
  PPE used

## Slide 122
Medical surveillance is a program of collecting and interpreting health data. It is required by law.
The Occupational Health and Safety Administration (OSHA) Hazardous Waste Operations and Emergency Response (HAZWOPER) standard, 29 CFR 1910.120.
The National Fire Protection Association’s (NFPA) NFPA 1500: Standard on Fire Department Occupational Safety and Health Programs addresses the health and safety of fire fighters and emergency medical care providers.
Environmental Protection Agency (EPA) regulations provide additional protection for workers that are not covered by OSHA.
What is medical surveillance?
1

## Slide 123
  A. clings to or saturates parts of your body or clothing.
1. EXPOSURE occurs when a toxic substance...
2. CONTAMINATION occurs when a toxic substance…
B. is taken into or is in direct contact with your body.
Match the correct answers.
What is the difference between exposure and contamination?
1

## Slide 124
BOTH!
Would you be exposed or contaminated working around this overturned pesticide truck?
1

## Slide 125
The process of removing or neutralizing contaminants that have accumulated on personnel and equipment.
What is decontamination?
1

## Slide 126
1. Leave the Hazard Area.
2. In the selected Decontamination Area:
Keep SCBA on and in use.
Brush off heavy particles of material.
Use handline without nozzle to rinse SFPC, top down.
After thoroughly rinsing, step into the clean area.
3. In the Clean Area
Remove SFPC.
Make sure you remove SCBA facepiece last.
4. At Quarters
Take a personal hygiene shower.
Don a clean uniform.
Clean and inspect your SFPC and SCBA.
Name the steps for decontamination.
CONTAMINATION
DECONTAMINATION
4

## Slide 127
1. Dry contaminants should be brushed off the skin.
6. If a contaminating substance is not water-soluble, wash the skin (never the eyes) with soapy water.
Name the steps for emergency decontamination.
CONTAMINATION
DECONTAMINATION
2. Flush affected skin and mucous membranes (including eyes) with water—large amounts when corrosives are involved.
3. Remove outer clothing if not easily decontaminated.
4. Flush victims again with water.
5. When many areas of the body are affected, give priority to the most vulnerable areas, like the eyes.
6

## Slide 128
The two primary components of PPE (Personal Protective Equipment) are: SFPC and SCBA. What are their limitations as protective equipment?
SCBA provides respiratory protection.
However, its bulk and weight hinder maneuverability.
It has a limited air supply.
High temperatures can compromise its effectiveness.
PPE (Personal Protective Equipment)
SFPC
SCBA
2
SFPC protects you from heat and flame.
However, it is easily permeated by most hazardous chemicals.
Contaminants may not be removed by cleaning.

## Slide 129
1. Skin absorption
Identify two factors that affect each route of exposure.
3. Ingestion
2. Inhalation
4. Injection and puncturing
* The eyes are also routes of toxic exposure.
Rate of breathing
Depth of breathing
Swallowing toxic materials
Eating before completion of decontamination
Jagged glass or metal
Syringes
High-pressure devices
Skin temperature/ blood flow
Higher concentration = greater exposure
Areas w/ more hair = more exposure
Length of exposure
Type of chemical
What are the four major routes of entry of hazardous materials?
5

## Slide 130
Asphyxiants
Corrosives
Irritants
Sensitizers
Carcinogens
Biological hazards
Radiological hazards
Neurotoxins
cause damage to the central or peripheral nervous system
For the following categories of toxic chemicals, identify the effects they may have on the body.
prevent oxygen use by the body
can cause irreversible tissue damage
cause uncomfortable to fatal effects
cause skin rashes or asthma-like reactions
cause cancer
can cause hepatitis, HIV, herpes, or TB
can cause cancer
8

## Slide 131
Inhalation is a major route of exposure to chemicals:
Use SCBA as your primary means of respiratory protection.
Fit-test SCBA before use to maintain a positive pressure in the facepiece during inhalation and exhalation.
Secondary Contamination continues until everything exposed is decontaminated:
Patients must be decontaminated before emergency care is given.
Your equipment must be decontaminated before reuse.
If equipment cannot be decontaminated, it must be disposed of properly.
To prevent or minimize exposure to toxic materials, know the following:
2

## Slide 132
A commitment to your health ensures:
Less risk of death, injury or disabling disease
Improved physical performance
Decreased stress, tension and anxiety
Enhanced rest and sleep
Increased ability to bounce back from strenuous events
Pay daily attention to remaining as healthy as possible; reap the benefits in performance.
3
Key components of a proactive health strategy are:
Medical review
Fitness
Stress management
Nutrition
Physical fitness is critical to your ability to perform safely and effectively as an emergency responder.

## Slide 133
THE END
Knowledge of exposures and prevention
plus
Participation in a medical surveillance program
equals
A healthier and longer life.
Lesson learned from Unit 2?
0

## Slide 134: Personal Protective Equipment
The Following Items Offer You NO Protection What - So - Ever:
        Weapon
        Badge
        Flak Vest

## Slide 135
1. Define the objectives to develop a pre- incident plan
2. List resources to consider when preplanning.
3. Identify types of information needed in order to assess risks.
Key Learning Goals :
Planned Response Summary
5. Explain the importance of scene management at a HAZMAT incident.
4. List eight First Responder Actions.

## Slide 136
    What are the 3 steps in pre-incident planning?
1. HAZARD IDENTIFICATION.
• Identify all types and locations of hazards in the community or jurisdiction.
2. HAZARD ANALYSIS AND RISK ASSESSMENT. • Identify the potential for an incident that will cause damage to life, property, or the environment.
• Identify vulnerable areas and analyze the risk or probability of an incident.
3. ANALYSIS OF RESOURCES.
• Resources include everything needed to control an incident such as personnel, supplies, equipment, and funding.
3

## Slide 137
Moderate Risk for First Responders
Victims, Low Probability of Survival
When actions are directed toward the rescue of victims with low probability of survival, first responders should face only moderate risk.
Here, the appropriate decision is not obvious.
    Balancing risks and benefits at an incident
When actions are directed toward property conservation only, first responders should face only low risk. Risk nothing for property already lost.
Low Risk for First responders
Rescue Property Only
Possible High Risk for First Responders
Victims, High Probability of Survival
When actions are directed toward the rescue of victims with high probability of survival, first responders may be subjected to high risk. It is reasonable to face risks in order to save a life.
3

## Slide 138
Observe conditions upon arrival.
Use recognition and identification clues to determine the presence of hazardous materials.
Is the material spreading?
What hazards are likely to result from the spill or release?
Strategic priorities: Life safety (operating forces and civilians), incident stabilization, property and environment conservation.
First Responder Actions (FRAs) - An 8-step Process for Incident Management:
1. Establish command
2. Survey the scene
3. Collect / interpret information
4. Assess vulnerable population
5. Identify container damage
6. Isolate the hazard
7. Create an action plan
8. Continue to evaluate
    First Responder Actions
12
Secure the scene.
Establish controlled access areas.
Start at an outside perimeter and work toward isolation of the contaminated area.
1. Isolation Perimeter
2. Cold Zone
3. Warm Zone
4. Hot Zone
Evaluate container markings.
Estimate amount of hazardous materials present, form of the material, and point of release.
Consult at least three resources to compare recommended response actions.
Consider conditions at incident:
• Look for possible ignition source
• Evaluate accessibility
• Note weather conditions and wind
If contaminated individuals are rescued, then isolation, decontamination, and treatment must be arranged.
If an incident affects large groups of people, an Incident Commander must decide whether evacuation or in-place protection is most appropriate.
Rescue at HAZMAT incidents should not be performed unless the safety of rescuers can be assured.
Assess container from a location uphill and upwind. Look for:
• Rising sounds of pressure relief devices
• Paint discoloration on tanks
• Amount of product that may have escaped
Information may be available from employees or drivers at the scene of the incident.
Do not approach a container in order to collect this information.
First Responder actions for isolating hazards are limited to defensive tactics only.
Use any of these 6 defensive actions:
1. Extinguishment - use a variety of materials (e.g., water or foam)
2. Vapor suppression
3. Diking, damming, diverting, and retaining
4. Absorption
5. Dilution
6. Remote valve shutoff
An action plan requires quick decision-making based on a knowledge of:
    • PPE usage
    • Decontamination
    • Rescue/Recovery
    • Spill control techniques
    • Remote valve shutoff
    • Requesting additional resources
    • Fire control
8. Continue to evaluate - Utilize the APIE process to determine whether objectives are being met:
The APIE Process
STEP 1. Analyze the Problem
STEP 2. Plan the Response
STEP 3. Implement the Plan
STEP 4. Evaluate the Progress
THE END

## Slide 139: Always Survey Your Scene Be Aware of the Potential

## Slide 140: The “Green Pages”
Don’t forget to look for the “SPECIAL” information here.

## Slide 141: Remember The Rule of Thumb

## Slide 142
Reebok vs. Rambo

## Slide 143: Never A Crime to Stay Alive!

## Slide 144: What’s in that black smoke and Barrels?
Maybe a good time to use the rule of Thumb ?

## Slide 145: What’s NexT ?

## Slide 149: Are you too close to the Action?

## Slide 150: Decontamination is not Optional !

## Slide 151: Keep The big picture in focus
Downwind concerns
Location
Time of day
Duration
Contamination
Weather
Escape paths
Self Protection

## Slide 152: Meth Drug Labs An everyday risk

## Slide 153: What to lookout for !
Toluene found in paint thinner
Methanol
found in gas tank anti-freeze "Heet"
Ethyl Ether found in starting fluid
Anhydrous ammonia found at farmer's co-ops
Hydrochloric acid found in hardware stores
Lithium found in camera batteries
Ephedrine found in cold medicine or dietary supplements
Sodium hydroxide found in "Drano" or Red Devil Lye
Sulfuric acid found in battery acid or drain cleaners
Iodine crystals found in iodine crystals or tincture of iodine
Red phosphorous found in striker plates

## Slide 154: Don’t Expect “Good Housekeeping”

## Slide 155: Center For Disease Control Report
From 1996 to 1999 there were 23,327 total incidents involving hazardous substances as reported by 16 states. HSEES also reports that 112 events (0.5%) were associated with methamphetamine (meth) labs with all of these events occurring in the five following states; Iowa, Minnesota, Missouri, Oregon, and Washington. Additionally, these 112 events at meth labs produced 155 total injuries with 79 occurring to first responders. In other words, 51% of all injuries at meth labs happened to first responders.

## Slide 156: Meth Lab Injuries
The breakdown of 79 injuries to first responders is as follows;
    55 (69.6%) - Police 9 (11.4%) - Emergency Medical Technicians/Paramedics 8 (10.1%) - Firefighters 7 (8.9%) - Hospital Employees

## Slide 157: Lessons Learned
Washington In April, 1996 an oven exploded as two people were using acetone, hydrochloric acid, and sodium hydroxide to make methamphetamine "meth" in an apartment laboratory. One person received chemical burns and was taken to a hospital where three unknowing hospital employees were also exposed. They began vomiting and became incapacitated. Additionally, three ambulance personnel and two police officers received eye irritation and respiratory distress from their exposures. None of these people were wearing any personal protective equipment.